| ISO/IEC JTC1/SC17/WG8 | ISO/IEC JTC1/SC17 N 4060 |
| --- | --- |
| Contactless integrated circuit cards | ISO/IEC JTC1/SC17/WG8 N 1756 |

Report of the Convener of WG8

to the 23rd Plenary Meeting of ISO/IEC JTC1/SC17

being held in Takamatsu, Japan, 2010-10-06/08

Contents:

1.	Meetings since the last SC17 Plenary Meeting

2.	ISO/IEC 14443, Proximity cards (PICCs), and its related test methods 
	ISO/IEC 10373-6

3.	NP on “PICCs with external power supply”

4.	Harmonization of ISO/IEC 14443 and NFC standards

5.	ISO/IEC 15693, Vicinity cards (VICCs), and its related test methods 
    	ISO/IEC 10373-7

6.	Appreciations

7.	WG8 Website

8.	Next meetings

1.	Meetings since the last SC17 Plenary Meeting

Three WG8 meetings have been held since the last SC17 Plenary Meeting:

- 46th meeting of WG8 in Valence, France, 2009-12-02/04

Participation: 23 delegates from 7 countries and 2 Liaison Organizations, in detail:

Austria		2

France  		6

Germany  		5

Israel 			1

Japan  		5

Spain			1

U.K.   			1

EU JRC		1

Visa Europe		1

- 47th meeting of WG8 in Berlin, Germany, 2010-04-28/30

Participation: 26 delegates from 9 countries and 2 Liaison Organizations, in detail:

Austria		3

Finland		1

France  		5

Germany  		8

Israel 			1

Japan  		3

Spain			1

Switzerland		1

U.K.   			1

EU JRC		1

Visa Europe		1

- 49th meeting of WG8 in Takamatsu, Japan, 2010-09-29/10-01

Participation: 26 delegates from 11 countries and 1 Liaison Organization, in detail:

Austria		3

China			1

France  		5

Germany  		3

Israel			1

Japan  		7

Korea  		1

Singapore  		1

Spain  		1

Switzerland  		1

U.K.   			1

VISA Europe		1

During that period the Task Force TF2 of WG8, with its Convener Pascal Roux (France), has held three meetings:

- 31st meeting of WG8/TF2 in Valence, France, 2009-11-30/12-01. 
Participation: 22 delegates from 6 countries and 2 Liaison Organizations.

- 32nd meeting of WG8/TF2 in Berlin, Germany, 2010-04-26/27. 
Participation: 24 delegates from 7 countries and 2 Liaison Organizations

- 33rd meeting of WG8/TF2 in Takamatsu, Japan, 2010-09-27/28. 
Participation: 23 delegates from 7 countries

2.	ISO/IEC 14443, Proximity cards (PICCs), and its related test methods 
ISO/IEC 10373-6

  - ISO/IEC 14443-1:2008 (2nd Edition)

The 2nd edition of the standard:

ISO/IEC 14443-1:2008, Identification cards - Contactless integrated circuit cards - Proximity cards - Part 1: Physical characteristics

was published on 2008-06-15.

2.2	ISO/IEC 14443-2:2010 (2nd Edition)

The 2nd edition of the standard:

ISO/IEC 14443-2:2010, Identification cards - Contactless integrated circuit cards -Proximity cards - Part 2: Radio frequency power and signal interface

was published on 2010-09-01.

The request from the WG8 Convener and the responsible Project Editor to the ISO/IEC Secretariat to delay the planned publicaton of that standard had been ignored. Reason for the requested delay was that editorial mistakes had been found out in the proof copy of the version intended to be published. A list of needed corrections had been sent to the ISO/IEC Secretariat, but just a part of it had been implemented, so that the now published text still contains mistakes, luckily just minor ones. It will be checked in WG8, whether a corrigendum procedure will be necessary.

2.3	ISO/IEC 14443-3:2001

The 1st edition of the standard:

ISO/IEC 14443-3:2001, Identification cards - Contactless integrated circuit(s) cards - Proximity cards - Part 3: Initialization and anticollision

was published on 2001-02-01.

The 2nd edition could have been published already by the begin of 2010. Namely, its FDIS of had been approved by the end of 2009. Since then the editorial cooperation between the ISO/IEC Secretariat and the responsible Project Editor has been blocked. Tries to run an iterative editing process between both have failed. The currently available “final” version cannot be published yet, as several corrections have to be made and the list of relevant patents has to be revised.

2.4	ISO/IEC 14443-4:2008 (2nd Edition)

The 2nd edition of the standard:

ISO/IEC 14443-4:2008, Identification cards - Contactless integrated circuit cards - Proximity cards - Part 4: Transmission protocol

was published on 2008-07-15.

2.5	ISO/IEC 10373-6:2001

The 1st edition of the standard:

ISO/IEC 10373-6, Identification cards - Test methods - Part 6: Proximity cards

was published on 2001-05-15.

The 2nd edition has received an approved FDIS status on 28th August 2010. Usually the publication shouldn’t be a problem. However, it had been found out, that the FDIS text which  had been agreed by WG8 and then submitted to the ISO/IEC Secretariat via SC17 was mistakenly edited by the ISO/IEC Secretariat and then sent out for FDIS ballot. A close cooperation between the ISO/IEC Secretariat and the responsible Project Editor is now seen necessary for processing corrections before the publication of ISO/IEC 10373-6:2010 (maybe 2011!).

2.6	Amendments regarding “Electromagnetic disturbence” (EMD)

2.6.1	ISO/IEC 14443-2:2010/Amendment 3

ISO/IEC 14443-2:2010, Identification cards - Contactless integrated circuit cards - Proximity cards - Part 2: Radio frequency power and signal interface - Amendment 3:  Limits of electromagnetic disturbance levels

2.6.2	ISO/IEC 14443-3:2010/Amendment 4

Identification cards - Contactless integrated circuit cards - Proximity cards -

Part 3: Initialization and anticollision - Amendment 4: Electromagnetic disturbance handling

2.6.3	ISO/IEC 10373-6:2010/Amendment 9

Identification cards - Test methods - Part 6: Proximity cards - Amendment 9: Test methods for electromagnetic disturbances

All three above amendments

- have achieved approved FCD (FPDAM) status,

- their received comments have been resolved,

- will be launched as FDIS ballot (FDAM) by mid November 2010.

2.7	Amendments regarding “Additional PICC classes”

2.7.1	ISO/IEC 14443-1:2008/Amendment 1

Identification cards - Contactless integrated circuit cards - Proximity cards - Part 1: Physical characteristics - Amendment 1: Additional PICC classes

- has achieved approved FCD (FPDAM) status,

- is being launched as FDIS ballot (FDAM).

2.7.2	ISO/IEC 14443-2:2010/Amendment 4

Identification cards - Contactless integrated circuit cards - Proximity cards - Part 2: Radio frequency power and signal interface - Amendment 4: Additional PICC classes

- has achieved approved 2nd FCD (FPDAM) status,

- its received comments have been resolved,

- will be launched as 3rd FCD ballot (FPDAM) by mid November 2010.

2.7.3	ISO/IEC 10373-6:2010/Amendment 8

Identification cards - Test methods - Part 6: Proximity cards - Amendment 8: Additional PICC classes

- has achieved approved 2nd FCD status (FPDAM),

- its received comments have been resolved,

- will be launched as 3rd FCD ballot (FPDAM) by mid November 2010.

2.8	Amendments regarding “Exchange of additional parameters”

2.8.1	ISO/IEC 14443-4:2008/Amendment 1

Identification cards - Contactless integrated circuit cards - Proximity cards -

Part 4: Transmission protocol - Amendment 1: Exchange of additional parameters

- has achieved approved FCD (FPDAM) status,

- will be launched as FDIS ballot (FDAM) by November 2010.

2.8.2	ISO/IEC 10373-6:2010/Amendment 11

Identification cards - Test methods - Part 6: Proximity cards - Amendment 11: Exchange of additional parameters

- will be launched as CD ballot (PDAM) by mid November 2010.

2.9	Amendments regarding “Very high bit rate” (VHBR)

2.9.1	ISO/IEC 14443-2:2010/Amendment 1

Identification cards - Contactless integrated circuit cards - Proximity cards - Part 2: Radio frequency power and signal interface - Amendment 1: Bit rates higher than fc/16 and up to fc

- will be launched as CD ballot (PDAM) by mid November 2010.

2.9.2	ISO/IEC 14443-3:2010/Amendment 2

Identification cards - Contactless integrated circuit cards - Proximity cards - Part 3: Initialization and anticollision - Amendment 2: Bit rates higher than fc/16 and up to fc

- will be launched as CD ballot (PDAM) by mid November 2010.

2.9.3	ISO/IEC 14443-4:2008/Amendment 2

IIdentification cards - Contactless integrated circuit cards - Proximity cards - Part 4: Transmission protocol - Amendment 2: Bit rates higher than fc/16 and up to fc

- will be launched as CD ballot (PDAM) by mid November 2010.

  - ISO/IEC 10373-6:2001/Amendment 7

Identification cards - Test methods - Part 6: Proximity cards - Amendment 7: Test methods for ePassport

was published on 2010-03-15.

3.	NP on “PICCs with external power supply”

WG8 agreed on an NP for amendments to ISO/IEC 14443 and 10373-6, which deals with a backward compatible modulation method that makes use of an external power supply provided independently of the 14443 generated field energy. The resulted standard will be e.g. applicable for mobile phones, which either are equipped with an antenna of “Class 3” or smaller, and thus normally operate a weaker magnetic field compared with a “Class 1” antenna field available with ID-1 cards. The consequence is that mobile phones with very small 14443 antennas, either built-in or externally provided e.g. via a micro SD card, function maximally similar like usual ID-1 cards. Also SC6 and the NFC Forum may benefit from the result of that standardization project, once the NFC standards will become harmonized.

WG8 asks SC17 to launch the ballot of the prepared draft NP.

4.	Harmonization of ISO/IEC 14443 and NFC standards

After a one-year-study-group period in 2009 SC6/WG1 established an ad hoc group on harmonization of ISO/IEC 14443 and NFC in early 2010. That group is chaired by the Co-Conveners Mr. Reinhard Meindl and Mr. Yoshihisa Takayama.

The progress of the harmonization can be seen positive and going into the right direction. It is hoped that the revised versions of ISO/IEC 18092 and 21481, plus related test methods, to be balloted under the usual ISO/IEC conditions, will be sufficiently defined, so that they can be applied e.g. to mobile phones, which are then able to act not only in modes defined in NFC, but also to act as a 14443 card (PICC) or a 14443 reader (PCD).

In order to improve the harmonization situation, SC17 decided at its plenary in 2008 that the WG8 Convener should get in contact with the NFC Forum Chaiman for investigating possibilities for the establishment of a Liaison between the NFC Forum and SC17. That investigation has become close to an end so that the establishment of that Liaison is likely to be realized by the end of 2010.

In addition WG8 decided on the following WG8 Resolution:

47.08	NP for specifying the specific needs of mobile devices using the 14443 interface

WG8 asks Mr. Rune Lindholm (Finland) and its Convener to investigate possible needs for mobile devices when using 14443, e.g. in its special capability to play the role of either a PICC or a PCD, and to prepare an NP for a related standardization activity. That draft NP will be circulated within the WG8 members for comments, before deciding to forward it to the SC17 Secretariat for NP balloting process.

5.	ISO/IEC 15693, Vicinity cards (VICCs) , and its related test methods 
ISO/IEC 10373-7

5.1	ISO/IEC 15693-1:2010 (2nd Edition)

The 2nd edition of the standard:

ISO/IEC 15693-1:2010, Identification cards - Contactless integrated circuit cards - Vicinity cards - Part 1: Physical characteristics

was published on 2010-10-01.

5.2	ISO/IEC 15693-2:2006 (2nd Edition)

The 2nd edition of the standard:

ISO/IEC 15693-2, Identification cards - Contactless integrated circuit cards - Vicinity cards - Part 2: Radio frequency power and signal interface

was published on 2006-12-04.

5.3	ISO/IEC 15693-3:2009 (2nd Edition)

The 2nd edition of the standard:

ISO/IEC 15693-3, Identification cards - Contactless integrated circuit cards - Vicinity cards - Part 3: Anti-collision and transmission protocol

was published on 2009-04-15.

  - ISO/IEC 10373-7:2008 (2nd Edition)

The 2nd edition of the standard:

ISO/IEC 10373-7, Test methods - Part 7: Vicinity cards

was published on 2008-05-01.

6.	Appreciations

Again WG8 expresses its thanks

-	to all the Project Editors of the WG8 standards, who have guided the WG8 delegates so well through plenty of ballot comments and provided excellently the many standard drafts,

-	to the SC17 Secretary for his very helpful and reliable guidance and

-	to the NBs of France, Germany and Japan, for having let WG8 and its Task Force TF2 meet in their countries under excellent conditions.

7.	WG8 Website

The WG8 website consists basically of two sections, one of which is public and the other one is password protected.

The public section consists of general information about the structure of WG8, its projects, meeting dates, and documents lists. This section can be accessed via the URL:

http://wg8.de

Any person authorized by a National ody can request the ID/password for accessing the WG8 website from the WG8 Secretariat via e-mail to office@wg8.de .

8.	Next meetings

WG8 & TF2		both in the week 2011-03-28/04-01	in Ispra, Italy

WG8 & TF2		both in the week 2011-09-26/30		in Song-Do, Korea

Michael Hegenbarth

Convener ISO/IEC JTC1/SC17/WG8