Editor Notes:

This document composes all comments to the "Ballot Result: ISO/IEC PDAM 14443-4:2008/Amendment X: Identification cards - Contactless integrated circuit cards - Proximity cards - Part 4: Transmission protocol - Amendment X: Frame with error correction." as submitted as WG8N1931 = SC17N4615.

Furthermore the "Corrected and Improved comments to CD 14443-4:2008/PDAM4" from Austria as submitted as WG8N1939 are copied in this summary file. These corrected (AT14 impr., AT15 impr. and AT18 impr.) and new (AT11a and AT19new) comments are marked with grey back ground. There are also both, the original and new figures and the new source code sample from Austria within this summary of comments. The WG8 attendees will decide whether to allow these comments or not.

I have also added a Note to AT11 comment as outcome of the TF2 meeting, not to forget, that it is not allowed to activate standard frame and frame with error correction in one direction at once.

Minor editorial comments I have already integrated in the new text of this amendment. I have written "Accepted" in the proposed editors disposition column.

| FR1 | 4 |  | ed | The use of italics for matrixes is not consistent between clause 4, the text and the figures | Update the symbols+text and/or the figures in accordance with ISO rules. |  |
| --- | --- | --- | --- | --- | --- | --- |
| FR2 | 4 |  | ed | cn does not represent all Hamming control bits but only bit n | Replace cn Hamming control bits with cn Hamming control bit n Same comment for "dn data bits" | Accepted |
| FR3 | 4 |  |  | hm.n is not used in the text 𝐻′𝑚 ,𝑛 is used in the text - matrix H' - upper case - comma between m and n - italics? | Replace hm.n element in row m and column n of matrix H with H'm,n element in row m and column n of matrix H | Accepted |
| FR4 | 4 |  | ed | No upper case letter for "Vector" | Replace Vector containing with vector containing (twice) | Accepted |
| FR5 | 4 |  | ed | Consistency with 14443-3 INF INFormation field belonging to higher layer | Replace LEN two bytes Length field used within enhanced block with LEN two bytes LENgth field used within enhanced block | Accepted |
| FR6 | 4 |  | ed | No upper case letter for "Matrix" | Replace I6x6 6 by 6 Identity Matrix with I6x6 6 by 6 Identity matrix | Accepted |
| FR7 | 7.1 |  | ed | Chapter means clause and is not used in ISO | Replace Replace first chapter with with Replace first paragraph with | Accepted |
| AT1 | Clause 7.1 | First sentence | ed | Spelling error | Replace "transmission" With "transmission" | Accepted |
| AT2 | Clause 7.1 | Last dash | ED | For the four byte mandatory epilogue field "(mandatory)" is missing | Replace last dash with: "and an four-byte epilogue field (mandatory). |  |
| FR8 | 7.1 |  | ed | Consistency | Add missing comma after a length field (mandatory) |  |
| US | Page 14, Clause 7.1 | All | T | and a four-byte epilogue field. “ should be Mandatory | Add “Mandatory” |  |
| FR9 | 7.1 |  | ed | Only one "and" in a sentence | Replace Add a new figure 15 and renumber all figures and add new clause 7.1.1 and renumber all clauses. with Add a new figure 15, renumber all figures, add new clause 7.1.1 and renumber all clauses. | Accepted |
| JP1 | 7.1 | new Figure 15 | ed | The explanation for the brackets is missing. | Add the following description in the new Figure 15; “NOTE The items in brackets indicate optional requirements.” |  |
| AT3 | 7.1.1 |  | ED | Length Field definition: It is not described how the length is measured  bits, bytes | Replace first sentence with: "The two-byte length field shall contain the sum (number of bytes) of lengths of:" |  |
| FR10 | 7.1.3 |  | ed | 7.1.3 is renumbered to 7.1.4 | Replace Page 18, Clause 7.1.3 with Page 18, Clause 7.1.3 (renumbered to 7.1.4) and show 7.1.4 in the new text |  |
| AT4 | Clause 10 | Figure 33 | ed | Should be Figure 27 | Renumber all Figures and update references to figures. |  |
| FR11 | 10.1 |  | ed | Reference error | Replace after their activation specified in 10.4 with after their activation specified in 10.5 | Accepted |
| AT5 | 10.2 | Title | ed | Title of Amendment is Frames with error correction, therefore "extended" is misleading. | Remove "extended" |  |
| JP2 | 10.2 |  | ed | The definition and purpose of “SYNC” is missing in this document. | Insert the explanation “SYNC” in clause 4 “Symbols and abbreviated terms” |  |
| JP3 | 10.2 | Figure 33 | ed | “SOC” is not defined in ISO/IEC 14443 series. In ISO/IEC 14443-3 Type-A, “S” is used for “start of communication” | Replace “SOC” by “S” |  |
| AT6 | 10.3 | Title | ED | Title of Amendment is "Frames with error correction". Therefore "extended" is misleading. Furthermore we should be clearer that for type B the frame format is for both directions. | Change Title to: "Type A PCD frame format for bit rates greater than fc/16 and Type B PCD and PICC frame format for all bit rates" |  |
| JP4 | 10.3 |  | ed | Though there is a description “SYNC sequence as defined in 10.2 transmitted as characters as defined in ISO/IEC 14443-3;”, the relation between this sentence and the description defined in ISO/IEC 14443-3. There is no definition for “SYNC” in ISO/IEC 14443-3. | Correct the description so that the relation between this sentence and the description defined in ISO/IEC 14443-3 will be clear. |  |
| FR12 | 10.3 |  | ed | typo | Missing semicolon after SOF | Accepted |
| AT7 | 10.3 | 3rd dash | ed | to be consistent to 10.2 3rd dash | Remove "bytes of" |  |
| AT8 | 10.3 | Last sentence | ed | Wrong reference | Replace "10.4" With "10.5" | Accepted |
| FR13 | 10.4.4 |  | ed | Typo (vector shall be underlined) | Replace remove column vectors h’n, with with remove column vectors h’n, with | Accepted |
| UK1 | General | Note on page 6 | ed | The sign ^ does not usually represent logical AND | Replace ^ with & |  |
| AT9 | Clause 10.4.4 | NOTE | ED | Logical is not the right description for the bit operator | Replace "logical" With "bitwise" |  |
| AT10 | Clause 10.4.5 | First paragraph | te | The content of dn is not clear | Add new sentence after first sentence: " d1 is bit b1 of the first byte and d56 is bit b8 of the seventh byte of any 7-byte sub-block from enhanced block." |  |
| FR14 | 10.4.5 | Figure 39 title | ed | The word "parity" stands for type A parity. "Hamming parity bits" are called " Hamming control bits" in this document | Replace Parity bits generation with Hamming control bits generation Check the whole document for similar replacement |  |
| FR15 | 10.4.6 |  | ed | consistency | Replace The parity check matrix H with The Hamming control check matrix H |  |
| US | 10.4.7 Error correction | all | E | “NOTE” should be followed by a colon | Add colons after “NOTES” |  |
| FR16 | 10.5 |  | ED | Reference to Figures 35 and 36 (in 1st dash and in table 6) seems wrong | Clarify if reference should be to figures 42 and 43 |  |
| AT11 | 10.5 | Table 6 | te | Framing options are only possible for frames with error correction. | Add new requirement in Table 6: "Framing options shall not be activated if standard frame format is selected." | Editors Note from TF2 Meeting: do only allow setting one frame format bit to (1)b. |
| AT11a (new) | 10.5 | Table 6 Table Footnote e) | te | When using SYNC, SOF/EOF and Start/Stop bit may be suppressed | Add to first sentence: ... when SYNC is suppressed." |  |
| AT12 | 10.5 | Figure 42 | ed | Remove "extended" frame | Use "frame with error correction" |  |
| FR17 | 10.5 |  | ed | Numbering of notes | There are 3 notes in 10.5. (except the note in table 6): they should be numbered 1, 2 and 3 |  |
| FR18 | 10.5 | Before figure 44 | ed | typo | Replace Standard and extended frame in both directions independent of each direction with standard and extended frame in both directions independent of each direction | Accepted |
| FR19 | 10.5 | Last note | ed | typo | Replace foot note with footnote (twice) | Accepted |
| AT13 | Annex D/E |  | ed | Due to new Annex D (bitrates > fc/2) Annex D will become Annex E and Annex E will become Annex F | Renumber Annexes |  |
| JP5 | Annex E | Title | ed | The title for whole Annex E and the one for E.1 are the same. | Reconsider the same title for whole Annex E and E.1. If there is no reason for this, remove the tile “E.1 Frame with error correction” |  |
| AT14 impr. | Clause D.1 | Last sentence | te | This information field leads to symmetric Hamming Control Bytes. | Replace in EXAMPLE '11' with '01' and '22' with '02'. The resulting CRC_32 = '8098F1FE'. |  |
| AT14 | Clause D.1 | Last sentence | te | Byte order is swapped twice | Replace last sentence with "Calculated CRC_32 = '19AA5D8F'." |  |
| AT15 impr. | Clause D.1 | Figure D.1 | te | This information field leads to symmetric Hamming Control Bytes. | Replace Figure D.1 with Figure AT1 from Annex AT_Comments |  |
| AT15 | Clause D.1 | Figure D.1 | te | Byte order is swapped twice | Replace Figure D.1 with Figure AT1 from Annex AT_Comments |  |
| AT16 | Clause D.2 | Method ComputeCrc32 | te | Byte order is swapped twice | Remove code lines before "return c;" starting at line with content "// revert byte order ..." |  |
| AT17 | Clause D.2 | Method main | ED | Byte order is swapped twice | Just to be clear to change byte order insert comment before last printf line: "// revert byte order to get least significant byte first" |  |
| AT18 impr. | Clasue E.1 | Figure 1 | te | This information field leads to symmetric Hamming Control bytes. | Replace Figure E.1 with Figure AT2 from Annex AT_Comments |  |
| AT18 | Clasue E.1 | Figure 1 | te | CRC byte order is wrong and Hamming Control bytes are wrong | Replace Figure E.1 with Figure AT2 from Annex AT_Comments |  |
| AT19 new | Annex E |  | te | To be more clear a code sample in C would be helpful | Add new Clause E.2 Code sample written in C language for Hamming Control Byte calculation From Annex AT_Comments |  |

Figure AT1 (new)

Figure AT1 (original)

Figure AT2 (new)

Figure AT2 (original)

NEW

## F.2 Code sample written in C language for Hamming Control Byte calculation

#include <stdio.h>

unsigned char ComputeHammingByte(unsigned char* pEnhancedSubBlock)

{

unsigned char currentByte;

unsigned char currentBit;

unsigned char c = 0x00; // Hamming control byte

unsigned char A[] = {   // Hamming control generation matrix A

0x03, 0x05, 0x06, 0x07, 0x09, 0x0A, 0x0B, 0x0C,

0x0D, 0x0E, 0x0F, 0x11, 0x12, 0x13, 0x14, 0x15,

0x16, 0x17, 0x18, 0x19, 0x1A, 0x1B, 0x1C, 0x1D,

0x1E, 0x1F, 0x21, 0x22, 0x23, 0x24, 0x25, 0x26,

0x27, 0x28, 0x29, 0x2A, 0x2B, 0x2C, 0x2D, 0x2E,

0x2F, 0x30, 0x31, 0x32, 0x33, 0x34, 0x35, 0x36,

0x37, 0x38, 0x39, 0x3A, 0x3B, 0x3C, 0x3D, 0x3E,

};

// iterate through all bits of the 7-byte sub-block from enhanced block

for (currentByte = 0; currentByte < 7; currentByte++) // 7 bytes

{

for (currentBit = 0; currentBit < 8; currentBit++)  // 8 bits each

{

// if bit is equal 1 XOR with corresponding column of matrix A

if ((pEnhancedSubBlock[currentByte] >> currentBit) & 0x01)

{

c = c ^ A[currentByte*8 + currentBit];

}

}

}

// add padding bits

c = (c << 1) | 0x81;

return c;

}

int main(void)

{

unsigned char EnhancedSubBlock[7] = {0x06, 0x00, 0x0A, 0x01, 0x01, 0x02, 0x80};

unsigned char HammingByte;

int i;

HammingByte = ComputeHammingByte(EnhancedSubBlock);

printf("\n");

printf("Hamming Control Byte reference results ISO/IEC 14443-4\n");

printf("Hamming Control Byte of enhanced sub-block [ ");

for(i=0; i<7; i++) printf("%02X ",EnhancedSubBlock[i]);

printf("] is %02X \n\n", HammingByte);

return 0;

}