Austria has just recognized, that the example given for "Frames with error correction" should be improved, as long as BOTH Hamming Control Bytes are symmetric. It is really important for interoperability, that the algorithm is widely implemented in the same way. So it is proposed to change the data in the information field from "11 22" to "01 02". To be consistent that is proposed also for the CRC32 calculation. Furthermore a "C" code for the calculation of the Hamming Control Byte is added.

The differences to the first submitted Austrian comments are marked below.

| AT1 | Clause 7.1 | First sentence | ed | Spelling error | Replace "transmission" With "transmission" |  |
| --- | --- | --- | --- | --- | --- | --- |
| AT2 | Clause 7.1 | Last dash | ED | For the four byte mandatory epilogue field "(mandatory)" is missing | Replace last dash with: "and an four-byte epilogue field (mandatory). |  |
| AT3 | 7.1.1 |  | ED | Length Field definition: It is not described how the length is measured  bits, bytes | Replace first sentence with: "The two-byte length field shall contain the sum (number of bytes) of lengths of:" |  |
| AT4 | Clause 10 | Figure 33 | ed | Should be Figure 27 | Renumber all Figures and update references to figures. |  |
| AT5 | 10.2 | Title | ed | Title of Amendment is Frames with error correction, therefore "extended" is misleading. | Remove "extended" |  |
| AT6 | 10.3 | Title | ED | Title of Amendment is "Frames with error correction". Therefore "extended" is misleading. Furthermore we should be clearer that for type B the frame format is for both directions. | Change Title to: "Type A PCD frame format for bit rates greater than fc/16 and Type B PCD and PICC frame format for all bit rates" |  |
| AT7 | 10.3 | 3rd dash | ed | to be consistent to 10.2 3rd dash | Remove "bytes of" |  |
| AT8 | 10.3 | Last sentence | ed | Wrong reference | Replace "10.4" With "10.5" |  |
| AT9 | Clause 10.4.4 | NOTE | ED | Logical is not the right description for the bit operator | Replace "logical" With "bitwise" |  |
| AT10 | Clause 10.4.5 | First paragraph | te | The content of dn is not clear | Add new sentence after first sentence: " d1 is bit b1 of the first byte and d56 is bit b8 of the seventh byte of any 7-byte sub-block from enhanced block." |  |
| AT11 | 10.5 | Table 6 | te | Framing options are only possible for frames with error correction. | Add new requirement in Table 6: "Framing options shall not be activated if standard frame format is selected." |  |
| AT11a | 10.5 | Table 6 Table Footnote e) | te | When using SYNC, SOF/EOF and Start/Stop bit may be suppressed | Add to first sentence: ... when SYNC is suppressed." |  |
| AT12 | 10.5 | Figure 42 | ed | Remove "extended" frame | Use "frame with error correction" |  |
| AT13 | Annex D/E |  | ed | Due to new Annex D (bitrates > fc/2) Annex D will become Annex E and Annex E will become Annex F | Renumber Annexes |  |
| AT14 | Clause D.1 | Last sentence | te | This information field leads to symmetric Hamming Control Bytes. | Replace in EXAMPLE '11' with '01' and '22' with '02'. The resulting CRC_32 = '8098F1FE'. |  |
| AT15 | Clause D.1 | Figure D.1 | te | This information field leads to symmetric Hamming Control Bytes. | Replace Figure D.1 with Figure AT1 from Annex AT_Comments |  |
| AT16 | Clause D.2 | Method ComputeCrc32 | te | Byte order is swapped twice | Remove code lines before "return c;" starting at line with content "// revert byte order ..." |  |
| AT17 | Clause D.2 | Method main | ED | Byte order is swapped twice | Just to be clear to change byte order insert comment before last printf line: "// revert byte order to get least significant byte first" |  |
| AT18 | Clasue E.1 | Figure 1 | te | This information field leads to symmetric Hamming Control bytes. | Replace Figure E.1 with Figure AT2 from Annex AT_Comments |  |
| AT19 | Annex E |  | te | To be more clear a code sample in C would be helpful | Add new Clause E.2 Code sample written in C language for Hamming Control Byte calculation From Annex AT_Comments |  |

Annex AT Comments

Figure AT1

Figure AT2

F.2 Code sample written in C language for Hamming Control Byte calculation

#include <stdio.h>

unsigned char ComputeHammingByte(unsigned char* pEnhancedSubBlock)

{

unsigned char currentByte;

unsigned char currentBit;

unsigned char c = 0x00; // Hamming control byte

unsigned char A[] = {   // Hamming control generation matrix A

0x03, 0x05, 0x06, 0x07, 0x09, 0x0A, 0x0B, 0x0C,

0x0D, 0x0E, 0x0F, 0x11, 0x12, 0x13, 0x14, 0x15,

0x16, 0x17, 0x18, 0x19, 0x1A, 0x1B, 0x1C, 0x1D,

0x1E, 0x1F, 0x21, 0x22, 0x23, 0x24, 0x25, 0x26,

0x27, 0x28, 0x29, 0x2A, 0x2B, 0x2C, 0x2D, 0x2E,

0x2F, 0x30, 0x31, 0x32, 0x33, 0x34, 0x35, 0x36,

0x37, 0x38, 0x39, 0x3A, 0x3B, 0x3C, 0x3D, 0x3E,

};

// iterate through all bits of the 7-byte sub-block from enhanced block

for (currentByte = 0; currentByte < 7; currentByte++) // 7 bytes

{

for (currentBit = 0; currentBit < 8; currentBit++)  // 8 bits each

{

// if bit is equal 1 XOR with corresponding column of matrix A

if ((pEnhancedSubBlock[currentByte] >> currentBit) & 0x01)

{

c = c ^ A[currentByte*8 + currentBit];

}

}

}

// add padding bits

c = (c << 1) | 0x81;

return c;

}

int main(void)

{

unsigned char EnhancedSubBlock[7] = {0x06, 0x00, 0x0A, 0x01, 0x01, 0x02, 0x80};

unsigned char HammingByte;

int i;

HammingByte = ComputeHammingByte(EnhancedSubBlock);

printf("\n");

printf("Hamming Control Byte reference results ISO/IEC 14443-4\n");

printf("Hamming Control Byte of enhanced sub-block [ ");

for(i=0; i<7; i++) printf("%02X ",EnhancedSubBlock[i]);

printf("] is %02X \n\n", HammingByte);

return 0;

}